RCB3Interface Library 1.0.4
(c) Laurent Lessieux

Notice

Use this library at your own risk. There is no guarantee this software would work at all in your system or your robot.
Your robot might be damaged.

Introduction

This is a library for controlling the RCB3 boards using the serial link from a PC under Windows.
The library is implemented in C in DLL form, RCB3_Interface.dll, so it can be used from almost any other language.

The library exports all functions documented by Kondo RCB3 Command Reference Manual.

The H file for C and C++ programers, RCB3_Interface.h, is included. It contains all necessary prototypes and constants to use the functions in the library.

The VB.NET and C# wrappers are also provided but not tested so far.

The LIB file necessary for linking is also provided with the name RCB3_Interface.lib.

This is a Low Level Library and as such each exported function map to one command of the protocol only.

Please refer to your Robot Software manual and RCB3 Command Reference Manual in order to understand concepts like position, motion, scenario, etc. An understanding of these concepts is necessary to use this library.

The DLL has been built using static lib in order to avoid any references to external DLL (except Kernel32.DLL).

Quick Summary of the RCB3 Board

The RCB3 board is able to control 24 servos and has 3 Analog to Digital converters that can be used.
It is also able to report the power supply voltage.

It has a bank of 5 scenarios and a bank of 80 motions.

Each scenario can have up to 200 motions.

Each motion can normally have “up to 30” slots. However you can overwrite the following motion's slots and therefore make longer motions.

All AD are 0 to 5V channels. The Power Supply off course goes higher since it's a 10.8V one.

The main connection is with the PC is done via the High Speed (115200bps) RC232 serial interface.

The RCB3 is also equipped with a second serial interface (2400bps) for the KRR1 remote control or other usages.

From the remote control, the RCB3 is able to receive buttons information as well as other things not documented here.

Each motion or scenario can have an associated buttons combination to start it. Don't ask me what's happening if you have multiple motions with the same buttons; it's probably taking the first one but I have not checked.

The RCB3 is also able to send notification every 0.5s for some data (ports running, AD values, remote control data), when enable you must poll the interface regularly to get the values.

Even if you don't the value will be stored into an internal buffer representing the last received data.

I won't go into details about Mixing and other exotic things here, it's outside the scope of this document.

Interface and Call protocol

I have decided to take a very secure approach for this DLL, so every call will return a boolean to indicate the succes or failure of the call.

If a failure occurs you can get an error value from GetLastRCB3Error(). You can also retreive a string associated with that specific error by using GetLastRCB3ErrorName(error value), but normally you are really interested in the full error message which can be obtained by GetLastRCB3FullErrorMessage().

For each call the following checks are done:

- Valid RCB3Interface passed
- Valid range for the input values
- Memory allocation failure (only necessary during the creation)
- NULL Pointer passed. (only 2 exceptions)
- Read/Write to input and output values passed by pointers are all protected via a try..catch block to ensure the validity of the pointer.
- Valid Model for this call
- valid checksum received from the RCB3

It is possible that some of my ranges check are incorrect so please don't hesitate to report any problem you think is range related.

In order to make it even clearer, I have prefixed the variable names with in_ or out_ to indicate which direction that goes.

How to use it

In order to access your robot using this library you must follow the next sequence:

1. Create an RCB3 interface
3. send command
4. check boolean for succes.
6. Send as many commands as you want
8. Destroy the RCB3 Interface

Since you need to specify the port, in theory you should be able to control more than one robot within the same program.

It is probably better to create the interface once and to keep it until you are done with it.
On creation, the interface will send a version request to the RCB3, if that fails then the creation will fail too.

Com ports can take any value, as long as it's working with HTH, it should be fine with the dll.

Internally the code will retry 3 times to get the acknoledgement from the RCB3 before sending the command, failure to answer within that time would result in a failure of the call.

Functions Details

Error Reporting:

UINT GetLastRCB3Error();

return the last error that occurred.

char* GetLastRCB3ErrorName(UINT error);

return a string with the describtion of the type of error.

char* GetLastRCB3FullErrorMessage();

return a string with detailled information about what failed.

Creation/Destruction of the Interface:

bool CreateRCB3Interface(int in_comPort,int in_comSpeed,int in_model,UINT &out_rcb3Interface);

First function that should be called to create an interface for the desired port.
The comSpeed should always be 115200.
The model should be one of the two currently supported ( RCB3_MODEL_NORMAL or RCB3_MODEL_J).

The out_rcb3Interface is the handle that will describe your new interface.
From now on, this number will be passed to all functions.

This function will try to open the COM port and communicate with the RCB3 to see if it is connected.

If the creation failed, take a look at the Error message to see what went wrong.

bool CreateRCB3InterfaceSkipCheck(int in_comPort,int in_comSpeed,int in_model,UINT &out_rcb3Interface);

Same as above but it will skip all the checks. That might allows you to send data to any intermediate module you might have.

bool CreateRCB3InterfaceViaBlueSmirf(int in_comPort,int in_comSpeed,int in_rcbmodel,int in_autodetectSpeed,int in_writeGoodConfigToFlash,int in_skipCheck,UINT &out_rcb3Interface);

Tentative code to interface with the BlueSmirf. It seems to work but I have too many errors with my interface to make it effective.

bool DestroyRCB3Interface(UINT in_rcb3Interface);

Delete the previously created interface and close the COM port.

Utilities:

//value of 0 or 1 for each. Usage depends on command too.
UINT RCB3MakeOption(UINT storeToEeprom,UINT forceMotion);

Construct the option value that needs to be passed to most of the functions.
The forceMotion is rarely used.

bool MakeMotionScenarioIndex(UINT &out_motionScenarioIndex,int motion = -1, int scenario = -1)

Some of the functions take a motionScenarioIndex, which represent either a motion or a scenario.
Motion are stored between 0 and 79 and scenario between 80 and 84.
This function is just a sum most of the time, but it could be usefull.

/////////////////////////
//Serial Extension
/////////////////////////

bool SendBytesToCOMPort(UINT in_rcb3,const char *in_buffer,UINT in_buffer_size);
bool ReceiveBytesFromCOMPort(UINT in_rcb3,char *out_buffer,UINT in_buffer_size);

These 2 functions allow you to communicate directly via the com port open for the interface.
That way you can extend the code as you want or dialog with a BlueTooth or Wifi Module if you have one connected.

Low Level Functions:

Software Switches:

bool SetRCB3SoftwareSwitch(UINT in_rcb3,UINT in_SWITCH,UINT in_option);

This function enables/disables quite a few things and can be written in ROM for default usage.
So here is the description of what in_SWITCH represents.

Bit 0: Sleep Mode, I have no idea what it does exactly and I have not tried it yet. However it's meaningless when writing to ROM
Bit 1: Suspension of the mouvement interpolation (No meaning when storing to ROM)
Bit 2: Periodic notification of data from RemoteControl. (0=OFF, 1=ON) (No meaning when storing to ROM)
Bit 3: Low Speed Serial Interface Mode: 0 = extended RCB3 protocol, 1=low speed serial KRC1, RCB1
Bit 4: 0
Bit 5-6-7: “setup cycle” from 0=15ms to 7=32.5ms by 2.5ms steps (No meaning for Type J board)
Bit 8: Periodic notification of Analog inputs data (0=OFF, 1=ON)
Bit 9: Periodic notification of motion data termination (0=OFF,1=ON)
Bit 10: Motion playback on Low Power (0=OFF,1=ON)
Bit 11:Motion Playback on Powe On (0=OFF,1=ON)
Bit 12:Motion playback on reset switch pressed (0=OFF,1=ON)
Bit 13:Control from remoteControl (0=OFF,1=ON)
Bit 14:ICS Mode (0=OFF,1=ON)
Bit 15: 0
Bit 16 to 31:0

bool GetRCB3SoftwareSwitch(UINT in_rcb3,UINT &out_SWITCH,UINT in_option);

Retreive the value explained in the precedent function.

//Motion/Scenario Playback
bool PlayMotion(UINT in_rcb3,UINT in_motionIndex,UINT in_option);
bool PlayScenario(UINT in_rcb3,UINT in_scenarioIndex,UINT in_option);

These two functions use the same low level command but I decided to create 2 functions for clarity purpose.
MotionIndex should be between 0 and 79
ScenarioIndex should be between 0 and 4

//Interruption of port motion (one bit set per port to stop)
bool StopPorts(UINT in_rcb3,UINT in_portsToStop);

Stops the current motion for all ports with a bit set to 1.
Bit 0-23 are only valid here.

//Set Port Speed and Position
bool SetPortSpeedAndPosition(UINT in_rcb3,UINT in_portIndex,UINT in_speed,UINT in_position,UINT in_option);

Set the position and speed for that port. That's what is used in HTH when changing the position with Sync on.
PortIndex between 0-23
Speed between 1-255 (0 is forbidden)
Position : well a 16bit value with a lot of meanings. See RCB3 Command Reference Manual.

bool SetPortsSpeedAndPosition(UINT in_rcb3,UINT in_motionIndex,UINT in_slotIndex,UINT in_speed,const UINT *in_position /*24*/,UINT in_option);

Same as above but for a slot in a motion.

bool GetPortsSpeedAndPosition(UINT in_rcb3,UINT in_option,UINT in_motionIndex,UINT in_slotIndex,UINT &out_speed,UINT *out_position/*24*/);

Reads the speed and position for that slot in the motion.

bool SetPortHomePosition(UINT in_rcb3,UINT in_portIndex,UINT in_homePosition,UINT in_option);
bool SetPortsHomePosition(UINT in_rcb3,const UINT *in_homePositions/*24*/,UINT in_option);
bool GetPortsHomePosition(UINT in_rcb3,UINT *out_homePositions/*24*/,UINT in_option);

Does what's in the name...

//Teaching
bool GetTeachedPosition(UINT in_rcb3,UINT *out_positions/*24*/);

It will probably return the position of each servos but I don't know what happen if you have not placed them in teaching mode before.

//Scenario Edition
bool SetMotionInScenario(UINT in_rcb3,UINT in_scenarioIndex,UINT in_slotIndex,UINT in_motionIndex,UINT in_option);

Write the motion index (0-79) into one of the possible slots (0-199) for the specified scenario (0-4)

bool GetMotionInScenario(UINT in_rcb3,UINT in_scenarioIndex,UINT in_slotIndex,UINT &out_motionIndex);

retreive the value from the scenario from that slot.

//Start switch/Power on Motion/Scenario
bool SetStartupMotion(UINT in_rcb3,UINT in_motionScenarioIndexSwitchPressed,UINT in_motionScenarioIndexPowerOn,UINT in_option);

When the switch has been set for these, you need to write which motion or scenario will be played in these cases.

bool GetStartupMotion(UINT in_rcb3,UINT &out_motionScenarioIndexSwitchPressed,UINT &out_motionScenarioIndexPowerOn);

See above.

//Low Power Configuration (in V)
bool SetLowPowerThresholdAndMotion(UINT in_rcb3,float in_lowPower,UINT in_motionScenarioIndex,UINT in_option);
Same as above but for the Low Power case.

bool GetLowPowerThresholdAndMotion(UINT in_rcb3,float &out_lowPower,UINT &out_motionScenarioIndex);

See above

//RCB3 version (last byte will always be zero
bool GetRCBVersion(UINT in_rcb3,char *out_version /*65*/);

Returns a string containing the version name and number. The string is normally 64 bytes but I extended it by one to make sure that I can store the 0 at the end.

//Analog Input
//outputs/inputs (In V)

bool GetAnalogInputs(UINT in_rcb3,float &out_power,float &out_ad1,float &out_ad2,float &out_ad3);

Retreives the measure values in V for the 3 AD channels and the power supply.

//Channel = 0,1 or 2
//Set to -1V for automatic detection but should not be done with ROM option
bool SetAnalogBaseValue(UINT in_rcb3,UINT in_channel,float in_baseValue,UINT in_option);
bool SetAnalogBaseValues(UINT in_rcb3,const float *in_baseValue /*3*/,UINT in_option);
bool GetAnalogBaseValues(UINT in_rcb3,float *out_baseValue /*3*/,UINT in_option);

Set/Get the base value, when you want to use the automatic detection then you must not use the ROM option and you must pass -1.0f to enable it.

//RealTime Mixing
bool SetRealTimeMixing(UINT in_rcb3,UINT in_channel,const UINT *in_mixingFactors/*24*/,const UINT *in_reverseFactor/*24*/,const UINT *in_set/*24*/,UINT in_option);
bool GetRealTimeMixing(UINT in_rcb3,UINT in_channel,UINT *out_mixingFactors/*24*/,UINT *out_reverseFactor/*24*/,UINT *out_set/*24*/,UINT in_option);

Configuration of the Realtime Mixing.
The valid channels are 0-2.
The mixing factor should be between 0-63
The reverseFactor should be 0 or 1: 0 for multiply by 1, 1 for multiply by -1
in_set should be 1 to enable the realtime mixing.

//Configuration of Motion playback on AD Deltas.
//0 or 1 to enable or disable motion playback

bool SetMotionPlaybackforAD(UINT in_rcb3,const UINT *in_motionScenarioIndices/*6*/,
        const UINT *in_levels/*6*/,
        const UINT *in_reverse/*6*/,
        const UINT *in_mixingSwitch/*6*/,
        UINT in_option);

bool GetMotionPlaybackforAD(UINT in_rcb3,UINT in_option,
        UINT *out_motionScenarioIndices/*6*/,
        UINT *out_levels/*6*/,
        UINT *out_reverse/*6*/,
        UINT *out_mixingSwitch/*6*/
        );
Enable you to activate motions automatically once a threshold has been reached for the specified AD channel.
I have no experience with that so I can't tell much more.

//Remote Control
bool GetDataFromRemoteControl(UINT in_rcb3,char *out_remoteControl/*7*/);
bool SetDataFromRemoveControlOverwrite(UINT in_rcb3,UINT in_option,UINT in_button,const UINT *in_analogChannel/*4*/);

Retreives or Overwrites the data from the remoteControl.
You will have to dig a bit in the manual for more information. But it seems that you can overwrite the button that is being pressed as well as 4 possible other values.

//Serial Extension
bool SetSerialExtensionAnalogBaseValues(UINT in_rcb3,const UBYTE *in_baseValue/*4*/,UINT in_option);
bool GetSerialExtensionAnalogBaseValues(UINT in_rcb3,UINT in_option,UBYTE *out_baseValue/*4*/);

It seems that via the extended serial protocol, one could get 4 more AD channels but on a 8bit range only.
This call would set the base value for them.

//ICS Mode
//1 bit per port
bool SetPortsInICSMode(UINT in_rcb3,UINT in_portsInICS,UINT in_option);
bool GetPortsInICSMode(UINT in_rcb3,UINT &out_portsInICS);

Set a port in ICS Mode.

//RedVersion Port configuration
bool SetRedVersionConfiguration(UINT in_rcb3,UINT in_portNumber,UBYTE in_backup,const UBYTE *in_stretch/*3*/,
        const UBYTE *in_speed/*3*/,UINT in_pulsePunch,UINT in_deadBand,UINT in_damping,
        UINT in_protectionTime, UINT in_reverse,
        UINT in_lowerPositionLimit,UINT in_upperPositionLimit,
        UINT in_freeTime);

bool GetRedVersionConfiguration(UINT in_rcb3,UINT in_portNumber,UBYTE &out_backup,UBYTE *out_stretch/*3*/,
        UBYTE *out_speed/*3*/,UINT &out_pulsePunch,UINT &out_deadBand,UINT &out_damping,
        UINT &out_protectionTime, UINT &out_reverse,
        UINT &out_lowerPositionLimit,UINT &out_upperPositionLimit,
        UINT &out_freeTime);

Configuration of the RedVersion Servos.
Don't ask me, I have no idea.
See The RCB3 command Reference Manual for details
//Serial Servo Port configuration

//Scenario Port used:
bool SetSerialServoPortUsage(UINT in_rcb3,UINT in_portsUsed,UINT in_option);
bool GetSerialServoPortUsage(UINT in_rcb3,UINT &out_portsUsed);

bool SetSerialServoConfiguration(UINT in_rcb3,UINT in_portNumber,UBYTE in_backup,const UBYTE *in_stretch/*3*/,
        const UBYTE *in_speed/*3*/,UINT in_pulsePunch,UINT in_deadBand,
        UINT in_damping,UINT in_protectionTime, UINT in_reverse,
        UINT in_lowerPositionLimit,UINT in_upperPositionLimit,
        UINT in_freeTime,UINT in_stretchSIO,UINT in_speedSIO,
        UINT in_offset,UINT in_ID, UINT in_p1,UINT in_p2, UINT in_n1, UINT in_n2);

bool GetSerialServoConfiguration(UINT in_rcb3,UINT in_portNumber,UBYTE &out_backup,UBYTE *out_stretch/*3*/,
        UBYTE *out_speed/*3*/,UINT &out_pulsePunch,UINT &out_deadBand,
        UINT &out_damping,UINT &out_protectionTime, UINT &out_reverse,
        UINT &out_lowerPositionLimit,UINT &out_upperPositionLimit,
        UINT &out_freeTime,UINT &out_stretchSIO,UINT &out_speedSIO,
        UINT &out_offset,UINT &out_ID, UINT &out_p1,UINT &out_p2, UINT &out_n1, UINT &out_n2);

Configuration of the Serial Servos.
Don't ask me, I have no idea.
See The RCB3 command Reference Manual for details

bool GetSerialServoStretch(UINT in_rcb3,UINT *out_stretch/*24*/);
bool GetSerialServoSpeed(UINT in_rcb3,UINT *out_speed/*24*/);

Don't ask me, I have no idea.
See The RCB3 command Reference Manual for details

//PDS Servo Port configuration
bool SetPDSConfiguration(UINT in_rcb3,UINT in_portNumber,UBYTE in_backup,UINT in_stretch,
        UINT in_speed,UINT in_pulsePunch,UINT in_deadBand,UINT in_damping,
        UINT in_failSafeTime,
        UINT in_lowerPositionLimit,UINT in_upperPositionLimit
        );

bool GetPDSConfiguration(UINT in_rcb3,UINT in_portNumber,UBYTE &out_backup,UINT &out_stretch,
        UINT &out_speed,UINT &out_pulsePunch,UINT &out_deadBand,UINT &out_damping,
        UINT &out_failSafeTime,
        UINT &out_lowerPositionLimit,UINT &out_upperPositionLimit
        );

Configuration of the PDS Servos.
Don't ask me, I have no idea.
See The RCB3 command Reference Manual for details

bool SetPDSPortsInUse(UINT in_rcb3,UINT in_pdsPortsInUse,UINT in_option);
bool GetPDSPortsInUse(UINT in_rcb3,UINT &out_pdsPortsInUse);

Set or Get which port is in PDS Mode.

//Default Port Position
bool SetPortsDefaultPosition(UINT in_rcb3,const UINT *in_defaultPositions/*24*/);
bool GetPortsDefaultPosition(UINT in_rcb3,UINT *out_defaultPositions/*24*/);

Should be self explanatory.

//Port Names
bool SetPortName(UINT in_rcb3,UINT in_option,UINT in_portIndex,const char *in_name);
bool GetPortName(UINT in_rcb3,UINT in_portIndex,char *out_name /*32*/);

It seems you can give nicknames to you ports, Not sure how that would be useful. Anyway here is it.

//Motion/Scenario Edition
bool SetMotionScenarioData(UINT in_rcb3,UINT in_option,UINT in_motionScenarioIndex,UINT in_moveCount,UINT in_portsUsed,
        UINT in_minute,UINT in_hour,UINT in_day,UINT in_month,
        UINT in_button,const char *in_name /*32 max*/);

bool GetMotionScenarioData(UINT in_rcb3,UINT in_motionScenarioIndex,
        UINT &out_moveCount,
        UINT &out_portsUsed,
        UINT &out_minute,UINT &out_hour,UINT &out_day,UINT &out_month,
        UINT &out_button,char *out_name /*32 max*/);

Set/Get the configuration for a Scenario. You must at least set the index you want to describe and the number of moves in the motiom/scenario.
I am not sure that the portsUsed are important for the scenario.
The time information, like the name can be set to anything it does not influence the motion/scenario.
The button information is the value that describes which button on the remoteControl should be pressed to start that motion/scenario.

//Timer based Notification (0.5s) when activated in the Software Switches.

bool GetLastDataFromRemoteControl(UINT in_rcb3,char *out_remoteData /*7*/);

Return the last data send by the RemoteControl.

bool GetLastPortsStatus(UINT in_rcb3,UINT &out_portsDone,UINT *out_portMotionDone/*24*/);

Retreive the status of each port and the motion executed. A port set to 1 indicates that the motion has been completed.

bool GetLastPowerAndADValues(UINT in_rcb3,float &out_power,float &out_ad1,float &out_ad2,float &out_ad3);

Returns the values in V for the 3 AD channels and the power supply from the latest notification.

/////////////////////////
//Files Extension
/////////////////////////

bool LoadMotionFile(UINT in_rcb3,const char *in_motion_filename,UINT in_motion_index,UINT in_force_overwrite);

Reads a motion file and store in the specified slot. You are responsible for checking that the previous slot is not using that space. Please pass 1 to in_force_overwrite if you want to write in the slot even if it is already used.

bool LoadScenarioFile(UINT in_rcb3,const char *in_scenario_filename,UINT in_scenario_index,UINT in_force_overwrite);

Reads a scenari file and store in the specified slot. Please pass 1 to in_force_overwrite if you want to write in the slot even if it is already used.

bool LoadHomePositionFile(UINT in_rcb3,const char *in_homeposition_filename,UINT in_scenario_index,UINT in_force_overwrite);

Set the home position from a home position file created by H2H.

Warnings

The commands that store permanently information on the RCB boards do so by means of recording information on an EEPROM.
This EEPROM can be written many times but not infinite times. The number of times the EEPROM can be writen is about one million times so for most purposes it is not a limit. However when working with programs that can potentially write on the EEPROM several thousand times per second, that limit may be a problem. The library allows you to perform many writes in a short period of time so be careful to not entering long loops when using permanent writing functions.

Final Note:

For the moment, the source will remain in closed source. I might consider opening them later.
A Linux version might also see the light in the near future but I won't maintain it.
If you are interested in porting it to other systems then please contact me, I am sure we can arrange something.

HAVE FUN!

Thanks to:
Kondo for putting online the RCB3 Command Reference Manual
Inaki Castillo for his RCB1 interface (I have C&P some of his text too)
Lem From http://www.robots-dreams.com
Edmen (from http://robosavvy.com Forum ) for the beta testing.